dynamoDB: stormobj_index
11/10/16
# Summary
Indexes volumes in the s3 bucket odimh5_archive. Used for many parts of wv! Items and preliminary attributes are initially added by wv_prep (h5_size, stop_timestamp) and regrid in wv_process provides sig_refl and tilt information.
# Database Structure
Table name:	wxradar_stormobj_index
Partition Key:	radar_id (number: ID)
Sort Key:	subset_id (string: yyyymmdd_HHMM00_###)
Attributes:
  - start_timestamp (string) (seconds==00)
  - track_id (number)
  - storm_latlonbox (string)
  - storm_dbz_centlat (number)
  - storm_dbz_centlon (number)
  - storm_edge_lat (string
  - storm_edge_lon (string)
  - h_grid (number)
  - v_grid (number)
  1. volume (number) km3
  2. area (number) km2
  3. major_axis (number)
  4. minor_axis (number)
  5. orient (number)
  6. max_tops (number)
  7. max_dbz (number)
  8. max_dbz_h (number)
  9. mean_dbz (number)
  10. max_g_vil (number) kg/m2
  11. mass (number) kt
  12. max_sts_dbz_h (number)
  13. cell_vil (number) kg/m2
  14. max_mesh (number) mm
  15. max_posh (number) %

NOTE: all stats at multiplied by 10 and rounded
# Usage
- wv_process:	Writes entries to database
- wv_track:	Reads database to compute tracking
- wv_kml:	Filtering storms
- wv_clim:	Filtering storms